## Slide 1: Basic Troubleshooting

## Slide 2: Troubleshooting Mantra
What is the problem
What can cause the problem
How can I test it
Notes: This mantra or chant, is something a technician should walk through every time they hit a road block in troubleshooting an issue. Too often a technician never even gets the answer to the first item before they back up, load the shotgun and start shooting parts at the machine. Most of the time you will eventually find the part that solves the problem, but that is the least effective, most frustrating and expensive way to solve the issue. Lets work through these steps.

## Slide 3: Start with Symptom
Clients report symptoms
Paper jam
Error code
Copy Quality
Notes: Clients almost always provide symptoms. We can think of a symptom as a manifestation of the underlying issue. For example, if you have a fever, it could be a symptom of many diseases. If you combine fever, with an achy body, chills, trouble breathing, you might have the flu. If you have the same symptoms but with nausea and vomiting, it might be norovirus or a different type of the flu.
So just like a doctor would ask a variety of questions to diagnose the specific disease, we will want more information to diagnose what other symptoms are happening.

## Slide 4: Step 1
Start by collecting information
When does it happen
What happens
  Where does the paper stop
  What noises does it make
  What were you doing when it happened
  Can you make it happen
  Does anything else happen
Notes: These are just some of the questions that you may want to ask. The exact questions will vary depending on the original symptom. The better you can get at asking the correct questions, the better you will get at resolving issues.
Example - Company reported that the copier was making copies all by itself. The technician goes out and watches the copier and it never makes a copy by itself, and testing showed it was working perfectly. The customer calls back with the same issue. This time the technician asks when it makes a copy by itself, and it turned out that it only happened with one individual. The technician asks to speak with the person and has them show what they were doing when it made the copy. Turns out that the person was fairly large, and when they were reaching up to get supplies their body contacted the print button but they didn’t notice.
Some times you will need the customer to help document exactly when the problem occurs.
Example: Early in the days of plain paper faxing when many customers used a long distance carrier different from their local service provider, I sold a client a new fax. The Key Operators name was Debbie, and she called me to say that the machine had erased it memory. I asked her to reprogram it and let me know if it happened again. When the problem occurred again, I went out reviewed the machines operation, and everything checked out with out any defect. I contacted the manufacturer, and we did all of the testing they could think of and we still couldn’t duplicate the issue. I had purchased several of the same devices, so I swapped it out, and the new one still did the same thing. Finally I asked Debbie to keep detailed records of what happened at the same time as the machine erasing the memory. It turned out that if she dialed a number with more than 13 digits and sent a fax that didn’t go through, and she checked the status of the fax, the machine erased itself. Once we had that information, we could duplicate the issue, and the issue was escalated back to the factory who created new firmware.
Without Debbie’s help, we would probably never been able to resolve the issue.

## Slide 5: Let the device help
What information does the management list provide
Does the job log provide additional information
If you can create it, check sensors before touching the problem.

## Slide 6: Step 2
Try to duplicate the issue
Follow clients steps exactly
See if there is a pattern to failure

## Slide 7: Step 3
Isolate the problem
  Make the problem small
  Try the same thing but different
  What can cause the symptom
    Paper jam – hitting something
    Clutch or motor not working
    Sensor not seeing paper

## Slide 8: Problem Isolation
Once the problem is identified, there should be a limited number of items that could cause any issue
If you have to guess, guess cheap, guess easy

## Slide 9: Step 4
After identifying probable causes you want to test the possible causes
  I/O mode for motors, clutches, and sensors
  Use a meter to monitor voltage
  Change settings to see if that makes a difference
  Sometimes just want to make a difference